(Note to Specifier:  This specification has additional instructions included as Hidden Text.  To view this information, Select Tools, Options, and check Hidden Text in the Formatting Marks section of the View Tab.)

2004 MASTER FORMAT™ SECTION 06 06 40

Schedules for Architectural Woodwork

3form Profile [Tiles or Panels]

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification sections, apply to this Section.

summary

This Section includes the Architectural Woodwork as shown and specified in the described system(s): Adjust list below to suit Project

Feature Wall

Wall Cladding

Wall Sculpture

Partitions

Ceiling Feature

[Insert Item]

Related Sections include the following:

sAdjust list below to suit Project

Section 06 06 40 Schedules for Architectural Wall Panels; Section 06 06 60 Schedules for Plastic Fabrications; Section 06 06 70 Schedules for Structural Composites; Section 06 06 80 Schedules for Composite Assemblies

Section 09 54 00 Specialty Ceiling;

Section 10 11 00 Visual Display Surfaces; Section 10 21 00 Compartments and Cubicles;

submittals

General:  Submit the following in accordance with conditions of contact and Division 1 specification section 01 33 00 “Submittal Procedures”.

Product Data:  Submit manufacturer’s product data; include product description, fabrication information, and compliance with specified performance requirements.

Submit product test reports from a qualified independent 3rd party testing agency indicating each type and class of panel system complies with the project performance requirements, based on comprehensive testing of current products.  Previously completed test reports will be acceptable if for current manufacturer and indicative of products used on this project.

Test reports required are:

Flame Spread and Smoke Developed (ASTM E 84)

Shop Drawings:  Include plans, elevations, sections, panel dimensions, details, and attachments to other work.

Samples for Initial Selection:

Submit minimum 4-inch by 4-inch samples.  Indicate pattern and finish.

Samples for Verification:

Submit minimum 4-inch by 4-inch sample for each pattern/finish combination of Architectural Woodwork

Delete below if mockups are not required

Mockups:

Build mockups to verify selections made under sample Submittals and to demonstrate aesthetic effects.

Build mockup of [each type of] Architectural Woodwork.

Retain subparagraph below if mockups are erected as part of building rather than separately

Approved mockups may become part of the completed Work if undisturbed at time of Substantial Completion.

Maintenance Data:  Submit manufacturer’s care and maintenance data, including care, repair and cleaning instructions.  Include in Project closeout documents.

quality assurance

Manufacturers Qualifications

Materials and systems shall be manufactured by a company continuously and regularly employed in the manufacture of specified materials for a period of at least two (2) consecutive years and which can show evidence of those materials being satisfactorily used on at least three (3) projects of similar size, scope and location.  At least three (2) of the projects shall have been successful for use two (2) years or longer.

Manufacturer must offer a documented reclaim process that will take back, at the manufacturers cost, panels that are at their end-of life cycle.  Return process is preceded by following requirements highlighted in Section 02 42 00 Removal and Salvage of Construction Materials.

delivery, storage, and handling

Deliver Architectural Woodwork and specified items in manufacturer’s standard protective packaging.

Do not deliver Architectural Woodwork, components and accessories to Project site until areas are ready for installation.

Store materials in a flat orientation in a dry place that is not exposed to exterior elements.

Handle materials to prevent damage to finished surfaces.  Provide protective coverings to prevent damage or staining following installation for duration of project.

Project Conditions

Environmental Limitations:  Do not install Architectural Woodwork until spaces are enclosed and weatherproof, and ambient temperatures and humidity conditions are maintained at the levels indicated for Project when occupied for its intended use.

Materials must be acclimated in an environment of 65-75 degrees Fahrenheit with maintained relative humidity levels of 25-55% for at least 48 hours prior to beginning the installation.

Warranty

Manufacturer’s Special Warranty on polymer panel system:  Manufacturer’s standard form agreeing to repair or replace units that fail in material or workmanship within the specified warranty period.

Warranty Period:  1 year after the date of substantial completion.

The warranty shall not deprive the owner of other rights or remedies the Owner may have under other provisions of the Contract Documents, and is in addition to and runs concurrent with other warranties made by the Contractor under the requirements of the Contract Documents.

PRODUCTS

Manufacturer

Manufacturer:  3form, Inc., Salt Lake City, Utah, USA / telephone 801-649-2500

Materials

Profile [Panels | Tiles]

Flakeboard MDF

Starting Thickness: ¾”

Pattern to be carved as specified

Carved MDF to be wrapped in specified finish (or provided unfinished if specified)

Sheet minimum performance attributes:

Flame Spread and Smoke Developed (ASTM E 84).  Material must meet a minimum Class B rating.

Mounting

PANEL CLEATS

To install Profile panels to the wall using Panel cleats, first Panel cleats must be attached to the back of the Profile panel. Panel cleats should run the entire width of the panel. A minimum of (3) rows of Panel cleats are necessary per 8’ tall panel. Rows of Panel cleats should be situated on the top and bottom edge of the panel, with additional rows spaced evenly between. Solid wood “in-wall” blocking is required.

DIRECT SCREW ATTACHMENT

Profile wall panels can be attached to a wall by screwing directly through the panel. Construction mastic should also be used to supplement the screws.  It is required to leave a 1/16” gap between panels to allow for expansion and contraction of the wood panels. This technique should only be used on non-wrapped panels that will be painted in the field.  Holes in the panel should be pre-drilled and counter-sunk.  After screwing the panel to the wall, a non-shrinking filler like Bondo may be used to cover the holes.  Please note that non-shrinking filler should not be used between panels.  A flexible seam filler should be used in between panels. This method is limited to a maximum of 6 panels.

CONSTRUCTION MASTIC

If using an adhesive to glue the panels directly to the wall, it is required to leave a 1/16” gap between panels to allow for expansion and contraction of the wood panels. An industrial grade silicone such as Momentive SilGlaze II SCS 2800 can be applied to the back of the panels in combination with 3M 4496 foam tape. Silicone should be applied in dots as it needs moisture (air) to cure. Alignment of the panels prior to curing is important as the panels may not be re-aligned after curing. Panel installations more than 16’ wide should use panel cleats.

Miscellaneous Materials

General: Provide products of material, size, and shape required for application indicated, and with a proven record of compatibility with surfaces contacted in installation.

Cleaner:  Type recommended by manufacturer.

EXECUTION

examination

Examine substrates, areas, and conditions where installation of Architectural Woodwork will occur, with Installer present, for compliance with manufacturer’s requirements.  Verify that substrates and conditions are satisfactory for installation and comply with requirements specified.

installation

General:  Comply with manufacturer’s written instructions for the installation of Architectural Woodwork.

Utilize fasteners provided by manufacturer.

Install components plumb, level and rigid, scribed to adjacent finishes, in accordance with approved shop drawings and product data.

We recommend that installation is completed by a 3form Certified Installer. Contact 3form for more information or to get a quote.

cleaning and protection

Protect surfaces from damage until date of substantial completion.  Repair work or replace damaged work, which cannot be repaired to Architect’s satisfaction.

End of Section 06 06 40

Architectural Woodwork (AW-1)

Patterns:	[Replace with pattern name]

Finish:	[Replace with finish name]

Installation Type: 	[Wall][Partition][Ceiling]

Refer to www.3-form.com for expansion/contraction information.  This information is required for applications subjected to temperature variation.

Repeat Product Data Sheets as required to identify all Varia™ applications.